SAFE WORK METHOD STATEMENT

| Principal Researcher / Lab or Workshop Manager: Ray Clout (by proxy) |
| --- |
| Faculty: FEIT |
| Location(s): B11, Level 13 EIF Equipment Room |
| Name of Assessor: Ray Clout | Date: 10/05/2015 |

Work Description: Store ZnB (Zinc Bromide) barrels in room CB11.13.204

Before you start

Visual inspection of work area and identify hazards Check risk assessment and chemical risk assessment Locate and make familiar MSDS for chemical

Always

Lock room door when leaving room Defer to lab manager for approvals during work process Ensure lab manager is appraised of potential problems and consult for advice Check ventilation fans are operating (fans cannot be turned off from within the storage area) Check with lab supervisor for location of vent fan switches and isolators (if fans not operating) If working (decanting etc.) with the chemical follow points 5 & 6 specifically Ensure barrel screw lids are tight and secure (while barrels are new lids are sealed)

Never

Drink the coffee provided by lab manager Leave door open or unsecured when not in vicinity Allow vent fans to be inoperable for long periods of time

| Personal Protective Equipment Required |
| --- |
| [ x ] Gloves | [ ] Face shield |
| [ ] Safety glasses/goggles | [ x ] Respirator |
| [ x ] Safety footwear | [ ] Protective clothing |
| [ ] Hearing protection | Other: |

| Define the Projects/Tasks |
| --- |
| If moving barrels, place soft sling around barrel and hook to abbey crane Lift barrel onto pallet Use ratchet tie downs to secure barrel to pallet Place pallet jack under pallet and lift Conduct pallet jack to work area Use electric pump (provided for decanting) | Lifting equipment is borrowed from Aerodynamics lab…return to same when finished Electric pump located behind PECC unit |

When you finish

Clean up area by removing any waste and rubbish, into skip on level -1 (approval from lab manager first) Check barrel leaks or spills and clean up. Contaminated waste material is to be placed inside plastic bags and labelled Contaminated waste is to be disposed of correctly. Check with lab manager for details Return lifting equipment to home room Thank lab manager for use of equipment

Specific Assessments

Chemical risk assessment

[ ] Plant licenses

[ ] Certification/licensing of operator

| Supervisors signature | Printed name | Date |
| --- | --- | --- |
|  | Ray Clout | 10/05/2015 |